# Recommendations for processing
# depth-averaged currents
# estimated from underwater gliders
Lucas Merckelbach and Bartolome Garau
## Introduction
This document describes a set or recommendations on how to process the depth-averaged currents provided by underwater gliders in order to include these parameters as part of the catalog of distributable products obtained from this observing platform.

## Basic principle of operation
The different underwater glider models currently available on the market can provide a depth-averaged current estimation. While each one of those models uses a different technique to estimate currents, all of them share a basic principle.

While underwater, the glider estimates its own position by deduced reckoning, that is, integrating its movement along time. When surfacing, this estimation is compared with a GPS fix. The difference is assumed to be due to a depth-averaged water current that deviated the glider during the subsurface navigation.

## Recommendations
Each water current estimation (vx, vy), has to be associated to the previous proper dive. That is, the last two consecutive GPS fixes that fulfill the next requirements:
- are far apart in time more than a certain threshold to be defined (e.g. 10 - 20 minutes)
- the mean depth between them is more than a certain threshold to be defined (e.g. 5 meters)

Assuming the glider estimated water currents vector (vx, vy) after a proper dive, navigating between positions (lat0, lon0, time0) and (lat1, lon1, time1), the georeferenciation of these water current “observation” would be the mid-point between beginning and end of integration period:

watercurrents_lat = ( lat0 + lat1) / 2
watercurrents_lon = ( lon0 + lon1) / 2
watercurrents_time = (time0 + time1) / 2

The water current vector in that location in time and space can be expressed in cartesian or polar coordinates. If expressed in cartesian coordinates, the values provided would be the East and North components of the vector, and their standard names in the CF conventions would be the following:

watercurrents_water_vx (standard_name: eastward_sea_water_velocity)
watercurrents_water_vy (standard_name: northward_sea_water_velocity)

Should the polar coordinates options be preferred, the values provided would stand for magnitude and bearing components respectively:

watercurrents_water_speed (standard_name: sea_water_speed)
watercurrents_water_direction (standard_name: direction_of_sea_water_velocity)

Ancillary information should be also provided for the user to describe at which extend the value provided is integrated over a certain period of time.

watercurrents_integration_time = time1 – time0

Similarly, a depth-averaging notion should be provided as well. The mean depth during the subsurface navigation can be computed, and should be weighted based on how much time the glider spends at each depth. With the time weighting, this computation does not assume that the glider remains the same time at all different depths. Instead, there can be situations where the glider spends more time on a certain range of depths during the subsurface navigation. Examples of such a situation are:
- when approaching the coast and bathymetry following (more time in shallow waters)
- when tracking deep waters, and not climbing up to the surface layer (more time in deep waters)

watercurrents_mean_depth = sum(depth * deltaTime) / watercurrents_integration_time

Another ancillary information of interest would be the glider speed through the water. Due to the CF conventions, it might be necessary to describe it in polar coordinates instead of cartesian ones, since the later option is not supported

watercurrents_glider_speed (standard_name: platform_speed_wrt_sea_water)
watercurrents_glider_direction (standard_name: platform_orientation)

The glider speed provided in these variables is obtained from the difference between the distance between the initial and final GPS fixes and the drift due to currents during that integration period. Its computation would follow an approach similar to the next one:

deg2m = 60 * 1852
meanLat = (lat0 + lat1) / 2
yDist = (lat1 - lat0) * deg2m
xDist = (lon1 - lon0) * cosd(meanLat) * deg2m
glider_vx = xDist - water_vx * watercurrents_integration_time
glider_vy = yDist - water_vy * watercurrents_integration_time

Then, the glider velocity with respect to water can be converted to polar coordinates:

watercurrents_glider_speed = sqrt(glider_vx^2 + glider_vy^2)
watercurrents_glider_direction = atan2(glider_vy, glider_vx)

As a suggestion, it would be advisable to keep coherency in the way velocities are expressed. Therefore, if platform speed has to be expressed in polar coordinates, water velocities could be expressed in the same way. That means, the polar coordinates option for water currents is preferred over the cartesian one.

It remains as an open question the problem of compass errors and magnetic declination, and its implications on all these computations.

## Real Time vs Delayed Mode procedures
Two modes of operation can be foreseen, depending on the availability of complete full-resolution datasets. In real time, the availability of data is critical. Real time systems generally have to deal with communication failures, connection drops, low bandwidth, etc. In delayed mode, it is usually common to have available all the information collected by the glider.

At this point, it is inevitable to make some distinctions between the different models available on the market. In real time, the Seaglider provides all the data (although connection drops are still an issue), while the Slocum only provides a subset of the information it collects. Conversely, in delayed mode, the information provided by the Slocum has a higher resolution, while the Seaglider remains the same.

So, the next two subsections describing the procedures are biased to the Slocum platform. A careful approach will be made to tackle the Seaglider as well, in case differences can be found between real time and delayed mode datasets.

### Real time procedure
The values provided by the glider are distributed without any correction. An uncertainty is also provided as an attribute of the variables. This uncertainty is obtained with the following procedure: historical datasets are analyzed, using a glider dynamics model described in [Merckelbach2010] to integrate glider speed through water including the angle of attack. With the new deduced reckoned position, new water currents are obtained and the difference with the original estimations is computed. The uncertainty provided will be related to the standard deviation of this distribution of differences.

The sensors m_water_vx and m_water_vy are recommended for real time, since they are computed and stored at the end of a segment, and therefore all the information is available to georeference them, both the currents and the dive. However, they include an error due to surface drift that cannot be accounted for until the next segment information arrives (which in real time, due to communication issues, may not happen).
### Delayed Mode procedure
The values provided by the glider are corrected for glider speed overestimation. The dataset is analyzed, using a glider dynamics model described in [Merckelbach2010] to integrate glider speed through water including the angle of attack. New water currents are obtained in delayed mode, m_final_water_vx/vy are used.

The estimation is better than the previous one, since they account for surface drift. However, each estimation belongs to the proper dive stored in the previous segment and that's why they are not recommended for real time. The corrected values should be stored in the following variables:

watercurrents_water_vx_adjusted
watercurrents_water_vy_adjusted
## References

[Merckelbach2010] Merckelbach, L.M., D.A. Smeed and G. Griffiths 2010. Vertical water velocities from underwater gliders. Journal of Atmospheric and Oceanic Technology 3(27), 547-563. DOI:10.1175/2009JTECHO710.1